## Slide 1: dfm_tools
Jelmer Veenstra
A Python package for D-FlowFM input and output

## Slide 2: dfm_tools: the concept
What:
  a Python package for pre- and postprocessing D-FlowFM input and output files
  contains convenience functions built on top of other packages like xarray, hydrolib-core and many more
Why:
  sharing of workflows among users (colleagues/external)
  no need to reinvent the wheel
  developments driven by projects like hydrolib-core, MassBay, FutureMares, TCOMS
Where:
  code on github: https://github.com/openearth/dfm_tools
  installable via pip
  jupyter notebooks and binder with example code

## Slide 3: xarray: io of netcdf files
lazy loading of netcdf files with knowledge of the entire structure
easy indexing over all dimensions with .isel() and .sel()
preprocess_his() enables indexing via station names (and other labels)

## Slide 4: xarray: io of netcdf files
easy indexing (subsetting)
easy and complete plotting
.../tests/examples/postprocess_hisnc.py

## Slide 5: HYDROLIB: io of D-FlowFM input files
Core scripts & tools for interaction with D-FlowFM:
reading/writing of (almost all) D-FlowFM input files (mdu, ext, bc, pli, etc)
full functionalities: https://deltares.github.io/HYDROLIB-core/0.3.1/topics/dhydro_support/
supported, documented, maintained
available on github: https://github.com/Deltares/HYDROLIB-core
users do not need to re-invent the wheel about “basic stuff/file formats”, focus on the analysis itself

## Slide 6: Examples: reading+plotting of D-FlowFM input files
hydrolib for reading files
conversion to xarray/pandas dataset with dfm_tools
figures: pli/pliz/ldb/tek and bc files
.../tests/examples/preprocess_hydrolib_readbc.py
.../tests/examples/preprocess_hydrolib_readwritepol.py

## Slide 7: Examples: interpolate oceanmodel to bc
xarray for reading netcdf data and .interp() to polyline points
hydrolib for reading pli and writing bc/ext files
.../tests/examples/preprocess_interpolate_nc_to_bc.py

## Slide 8: Application for regional models
Manually defined model boundaries, used for:
  Grid cut-out of GTSM (currently manual)
  Download of ERA5 and CMEMS field
  .../tests/examples/download_meteodata_oceandata.py
  Generation of (2D) open boundary forcing from FES2014 (tidal constituents)
  .../tests/examples/preprocess_interpolate_nc_to_bc.py
  Generation of (3D) open boundary forcing from CMEMS (salinity, temperature and sealevel anomaly)
  .../tests/examples/preprocess_interpolate_nc_to_bc.py
  Generation of 3D initial fields from CMEMS (salinity and temperature)
  .../tests/examples/preprocess_ini_cmems_to_nc.py
  Generation of meteorological forcing fields
  .../tests/examples/preprocess_meteo_mergenetCDFtime_xarray.py
The dfm_tools enables the quick set-up of the basis of a 3D model

## Slide 9: Examples: read+plot hisfile
xarray for reading hisfile (D-FlowFM and sfincs)
easy retrieval of lists of stations, cross_sections, general structures, etc thanks to preprocess_hisnc()
selection of data over dimensions: time, depth, stations, cross_sections, structures, etc
zt-plot (timeseries of one point with depth dim)
.../tests/examples/postprocess_hisnc.py
coming up:
  interpolation
  nesting

## Slide 10: Examples: read+plot mapfiles
supports flexible meshes (unstructured) map/fou/rst/net
supports partitions (handling of ghost cells)
select data based on variable and dimensions (time/layer/etc)
will be converted to xarray/xugrid for more convenience
satellite backgrounds with contextily
3D slicing: next slide

## Slide 11: Examples: slice trough 3D partitioned FM map data
given a polyline (blue)
slice trough 3D partitioned FM map data

## Slide 12: Examples: cartopy basemaps and coastlines/borders
support for almost any epsg

## Slide 13: Examples: vector plots for regulargrids
support for any other netCDF
e.g.: SFINCS, Delft3D4, oceanmodels, meteomodels

## Slide 14: Next steps
uitbreiding/improvements:
  support for D3D4? > overleg met Bert/Isabel
  extra models/sources for download/interpolate (evt xESMF for CMCC, climate forcing cmip6 procedure (=calendarconversion) and others)
  gebruikerswensen intern/rws/overig
  improvement of reading D-FlowFM mapdata (move to xarray and maybe xugrid, but mind partitions/slicing)
voorbeelden toevoegen:
  ini field uit 2D/3D map/rst
  gtsm voorbeeld?
  monthly/daily means or depth average of his/map fields (to show power of pandas/xarray)
  nesting biesbosch toevoegen: c:\DATA\dfm_tools_testdata\hydrolib_nc\bb_fact2_009a_net.nc
  nesting rmm/tcoms (interpolate map to obs/plipoints) (simple wl and z/sigma to z?) (400sec TK?)
  nesting FM in FM? (invdist interpolate his to obs/plipoints)
  Example notebook C-scale: https://github.com/c-scale-community/use-case-hisea/blob/main/notebooks/visualise_delft3dfm.ipynb

## Slide 15: Overlap afstemmen
dfm_tools (Jelmer Veenstra)
hydrolib-core (Arthur van Dam) > duidelijke afbakening
xugrid (Huite Bootsma) > duidelijke afbakening
DelftDashboard conversie naar Python (Maarten van Ormondt)
hydromt (Dirk Eilander)
tools van coastalhazardsteam (?)
D-FAST (Bert Jagers), vinden van cellen binnen zekere afstand van een lijn, projecties op een lijn, en doorsnijden van rooster met een lijn. https://iplo.nl/thema/water/applicaties-modellen/watermanagementmodellen/d-fast/
Pieter Koen: bob hoogendoorn notices many githubs/repos/etc